## Slide 1: Working with Change; Staying Current When Standards Change
APSG 43 - May 8, 2020
Kris Berglund
Vice-President, Sales

## Slide 2: Objectives
How GPS and GNSS technology changed geospatial data accuracy levels
Making old data match new data - common errors we see
iOGP geodetic data guidance for the O&G industry
  GIGS (Geospatial Integrity for Geoscience Software)
Future Standards? NGS and NSRS Modernization

## Slide 3
Global Positioning System (GPS) 2000, 24 satellites
GLONASS 1st in 1995, 2nd in 2011, 26 satellites
Galileo 2016, 30 satellites
BeiDou-3 2018, 33 satellites
GNSS
Global Navigation Satellite Systems
Regional Satellite Based Augmentation Systems (SBAS)
EGNOS (European Geostationary Navigation Overlay Service)
WAAS (Wide Area Augmentation System - U.S.)
MSAS (MTSAT Satellite Augmentation System - Japan)
GAGAN (GPS Aided Geo Augmented Navigation System - India)
SDCM (System for Differential Corrections and Monitoring - Russian Federation)

## Slide 4
Geospatial Data Accuracy
Accuracy
Positional accuracy
Attribute accuracy
Expected deviance in geographic location of object to true ground position
Feature accuracy in
relation to the elements
they represent (soil, forest cover, hydro, etc)

## Slide 5
Geospatial Data Accuracy Levels
Consumer grade GPS receivers (+/-3m)
Mapping grade GPS receivers (+/-1m)
Survey grade GPS receivers (+/-1cm/mm)

## Slide 6
Common Errors
Datum transformations
Rotation direction & method
Unit settings
Other assumptions

## Slide 7
Datum Transformations
Early binding & Late binding datum transformations
  Early binding - when transforming from datum A to datum B it uses intermediate datum as a “pivot” system (ITRF, WGS84)
  Late binding – No pivot system being used, direct transformation from the source datum to the destination datum
BUT…
  What if there is more than one transformation applicable to the two datums? (i.e. ED50 to ETRS89 there are multiple)
  Which WGS84? (G730, G873, G1150, G1674, G1762, Transit)
  Which ITRF Epoch?

## Slide 9
Rotation Direction and Method
Coordinate Frame Rotation vs. Position Vector Rotation
  Related specifically to 7 or 14-parameter datum shifts
  Achieves equal results, uses opposite method
  CFR is rotating the entire frame around the position
  PVR is rotating the actual position
BUT…
  What if one uses CFR when they need PVR?
  Reversed signage, improper calculation, bad positioning
Position Vector Rotation
Coordinate Frame Rotation

## Slide 10
Datum Transformation Parameters
Seven (7) Parameter Datum Transformation – shift happens
  Delta X, how much shift applied to geocentric X, + or – determines direction
  Delta Y, how much shift applied to geocentric Y
  Delta Z, how much shift applied to the geocentric Z
  Rotation X, denoted by angular units, defines rotation, + or – determines direction
  Rotation Y, denoted by angular units, defines rotation shift
  Rotation Z, denoted by angular units, defines rotation shift
  Scale, denoted by scale parameter
Fourteen (14) Parameter Datum Transformation
  Defines the relationship between 2 frames at a given instance in time
  Seven velocity parameters applied to the above shift/rotation/scale parameters

## Slide 11
Other Assumptions
Assumption of Equivalence
iOGP’s EPSG Geodetic Parameter Registry states:
WGS84 (All realizations), NAD83 (1986), NAD83(NSRS2007), NAD83 (2011),
ITRF (all epochs), GDA94, RGF95, JGD2000, IRENET95, ETRS89, etc…
…About 60 datums, worldwide are coincident at the +/- 1 meter level
Because of this, many tools are set up with that assumption.
Because of this, a lot of people are too.

## Slide 12
Geospatial Data Standard Organizations
Positional accuracy standards for digital geospatial data
Digital orthoimagery
Digital planimetric data
Digital elevation data
Data specifications for coordinate reference systems
Defines 2D, 3D, compound CRS
Map projection suggestions
Well known geodetic parameter dataset of ellipsoids, datums and datum transformations
Accessible online
Maintained by iOGP Geodesy Committee

## Slide 14
Using a Geodetic Registry
One source of approved geodetic objects
A registry is a central location for locating and verifying the right objects to use
Quickly search and locate objects based on certain criteria
      Location
      Known Area of Use
      Issuer codes (including EPSG codes)
      Object names
      Object types (units, ellipsoids, datums, prime meridians)

## Slide 15
Benefits of Using a Registry
What is the Right Registry?
  Single source of truth.
  It meets the internal requirements for access, editing & maintenance
  Something that supports internal CRS definitions, internal processes
  Quickly compare CRS definitions used by other vendors
  Use issuer codes to organize valid parameters used by other packages
Sharing Accurate Coordinate Reference System Definitions
  Organizational contractors, government partners, regulators, regional authorities
  Host your own registry for internal use

## Slide 17
GIGs
Geospatial Integrity for Geoscience Software
Defined
  Completeness. Proper geospatial metadata (CRS) required
  Correctness. Coordinate precision – free from error
  Consistency. Relates to data model, terminology
  Verifiability. Audit capability. Have the prior three been achieved?

## Slide 18: NSRS Modernization
  Four plate-fixed Terrestrial Reference Frames (TRFs)
    Plate rotation. Tectonic rotation around the Euler Point of a given plate (Euler Pole Rotation)
    An ITRF rotation model for each plate to negate plate rotation
    NEW PLATE-FIXED REALIZATIONS EVERY FIVE YEARS
  Intra-frame velocity models (IFVMs)
    Reflects all horizontal motions NOT due to Euler Pole Rotation
    Four IFVMs, one for each TRF
    Works with Horizontal Time Dependent Positioning (HTDP)
Notes: IGS = INTERNATIONAL GNSS SYSTEM
Intra Frame Velocity model will be how we compute the change over time to keep positions relative to the plate stable.
NATRF will agree with ITRF on the day it goes live, then will slowly drift away with the plate

## Slide 19
Thanks!
Kris Berglund, Vice-President, Sales
kb@bluemarblegeo.com
Notes: Bring up webinars and YouTube